## Slide 1: Massive MIMO Experiments
NSF PAWR POWDER Testbed
Bharath Keshavamurthy

## Slide 2: Experiment Topology: Anechoic Chamber
Compute Node for SSH and CTRL operations
[Dell PowerEdge R840 at the Fort Douglas Datacenter]
Iris clients (x2) inside the anechoic chamber
Massive MIMO (mMIMO) Base Station (BS | 48 Tx/Rx chains) and Aggregation Hub inside the anechoic chamber
MATLAB block-store sliver for toolbox-based development
A 10 Gbps Ethernet link between the compute node and the Faros Hub at the mMIMO BS for SSH access and control; similar link for both Iris clients

## Slide 3: mMIMO Resources: Iris SDR Standalone Configuration: Client | Daisy-Chained Configuration: mMIMO BS (Source: RENEW)

## Slide 4: mMIMO Resources: Daisy-chained Iris SDRs at the BS (Source: RENEW)

## Slide 5: mMIMO Resources: Skylark/Faros BS with Aggregation Hub (Source: RENEW)
RRH (Remote Radio Head) – also abbreviated as RH (Radio Head) – is an enclosure of several daisy-chained SDRs (e.g., 4).
Several of these enclosures (e.g., 6) constitute a mMIMO BS.

## Slide 6: mMIMO Development Layers (Source: RENEW)

## Slide 7: mMIMO Development Details
RENEWLab libraries, frameworks, and scripts:
  Radio Node (SDR) Discovery
  SoapySDR Middleware API for interfacing Python & MATLAB level control of the FPGA and ARM A9 processor within an Iris SDR
  Python Beacon Beam-sweeping, TDD Framer, and SISO Tx/Rx scripts
  C/C++ Sounder code – and its dependencies
  Python visualization & analysis tools
Our development:
  Compute node, Radio resource, and Frequency provisioning (Python | Rspec)
  RENEWLab Configuration & Control (Python | Shell | JSON)
  Modifications to Python-based visualization & analysis scripts (Python | Shell)
Yet to be tested:
  MATLAB toolbox-based development (TDD Frame Scheduler, Tx/Rx of Pilot Sequences, Channel Estimation, Beamforming, Modulation/Demodulation, Equalization, and Visualizations)

## Slide 8
LTE-signal SISO Tx/Rx at specific mMIMO BS SDRs

## Slide 9: LTE-signal SISO Tx
Starting LTE-signal Tx operations at a specific BS SDR (RF3E000246) | Frequency = 3.555 GHz
RF3E000246 Channel-A Tx chain initialization and calibration

## Slide 10: LTE-signal SISO Rx
Starting LTE-signal Rx operations at a specific BS SDR (RF3E000389) | Frequency = 3.555 GHz

## Slide 11: LTE-signal SISO Tx/Rx

## Slide 12: LTE-signal SISO Tx/Rx: Real-Time Visualizations

## Slide 13
TDD Framer

## Slide 14: TDD Framer
Initializing specific provisioned BS SDRs: LMS7002M transceiver startup
SDR-1 | Serial # = RF3E000246
SDR-2 | Serial # = RF3E000490
Both SDRs are at the mMIMO BS
Tx/Rx frequency | CBRS spectrum | 3.555 GHz
Frame schedule: Sinusoid pilot signal sent from one SDR (‘P’) | Received at the other SDR (‘R’) | Guard intervals in-between (‘G’)

## Slide 15: TDD Framer: Real-Time Visualizations

## Slide 16
mMIMO Beacon Beam-sweeping

## Slide 17: mMIMO Beacon Beam-sweeping: BS Operation (1)
Using Channel A on 5 SDRs at the mMIMO BS for this experiment
Frequency = 2.5 GHz | Tx gains = 81 dB | Rx gains = 65 dB
Configuring the BS SDRs that were explicitly provisioned in the script call

## Slide 18: mMIMO Beacon Beam-sweeping: BS Operation (2)
The 5x5 Hadamard beacon weight matrix
Write TDD configuration (‘BG’) to an SDR & BEACON_START

## Slide 19: mMIMO Beacon Beam-sweeping: BS Operation (3)
Manual termination of the script’s operation [expected behavior]
Power-down and Cleanup of all 5 provisioned SDRs

## Slide 20: mMIMO Beacon Beam-sweeping: Simultaneous Client Operation
A single standalone client is provisioned for the reception of these beacons from 5 BS-based SDR antennas (Channel-A)
Client configuration
Received beacon RSSI logging for an association heuristic
(E.g., Associate the client with the BS SDR whose signal has the highest RSSI value)

## Slide 21: mMIMO Beacon Beam-sweeping: Complete Console View

## Slide 22: mMIMO Beacon Beam-sweeping: Real-Time Visualizations

## Slide 23: A Full-scale Massive MIMO Experiment: Sounder
A sounder framework – with & without uplink data
  Use the concepts detailed earlier (SISO Tx/Rx, TDD Framer, Beam-sweep)
  48 BS antennas | 4 client antennas | Uplink data generation | HDF5 analyses
  The BS, the Aggregation Hub, and both clients are inside an anechoic chamber
  Record pilot signals from the 2 Iris clients received at all the antennas of the Skylark/Faros mMIMO BS ((6 RHs x 4 SDRs) x 2 Tx/Rx chains = 48 antennas)
  Post-process these recorded signals (HDF5 matrices) for channel statistics
  Visualize using Python scripts and MATLAB tool-boxes

## Slide 24
mMIMO Sounder
(with & without uplink data)

## Slide 25: mMIMO Sounder: Radio Discovery
6 RHs x 4 SDRs per RH = 24 SDRs x 2 Tx/Rx chains = 48 antennas at the mMIMO BS
2 standalone Iris SDRs as the clients

## Slide 26: mMIMO Sounder: JSON Configuration File
Faros Aggregation Hub ID: FH4B000021
Experiment Binding: Reserved Frequency Range
BS Daisy-Chained & Aggregated Iris SDR IDs: RF3E000246, RF3E000490, RF3E000749, RF3E000697, RF3E000724, RF3E000740, RF3E000532, RF3E000716, RF3E000674, RF3E000704, RF3E000676, RF3E000668, RF3E000340, RF3E000744, RF3E000161, RF3E000735, RF3E000387, RF3E000389, RF3E000206, RF3E000211, RF3E000256, RF3E000383, RF3E000304, RF3E000303.
Client SDR IDs
conf-bs-and-two-client.json

## Slide 27: mMIMO Sounder: Configuration Parameters
2 Tx/Rx channels per Iris SDR at the Base Station | 48 antennas in total at the Base Station
Center Frequency = 3555 MHz | Sample Rate = 5 Msps
Max Tx Gain at the Base Station = 81 dB | Max Tx Gain at a Client = 98 dB
Frame Schedule Details:
  Guard Interval (‘G’)
  Broadcast Beacon from the Base Station to the Clients (‘B’)
  Pilot from a Client to the Base Station (‘P’)
FFT Size for Pilot OFDM symbols = 64
Cyclic Prefix Length = 16
802.11 LTS-type pilot used for [fft_size = 64]
Number of OFDM symbols per slot = 10
OFDM symbol size = fft_size + cp_len = 80 samples
52 Non-Zero OFDM Sub-Carriers used in each OFDM symbol [fft_size = 64]

## Slide 28: mMIMO Sounder: Topology Confirmation
Make sure the serial numbers (IDs) of the Hub, the Base Station RHs and their constituent SDRs – along with the standalone clients are correct
One mMIMO Base Station: Designated Cell0
A Reference Node can be used at the BS for reciprocity calibration: not used here

## Slide 29: mMIMO Sounder: Start-up
Load the provided configuration: conf-bs-and-two-client.json
mMIMO BS Device Identification: 24 Iris SDRs | One Faros Aggregation Hub
Initializing the Standalone Iris Clients
Start the Sounder Application

## Slide 30: mMIMO Sounder: Setting up the Radios (1)
Standalone Iris Client-1 Setup
Standalone Iris Client-2 Setup
mMIMO BS SDRs Initialization

## Slide 31: mMIMO Sounder: Setting up the Radios (2)
mMIMO BS SDRs Setup
mMIMO BS SDRs Frame Schedule:
Beacon beam-sweep in the 1st frame;
Pilots from 4 client antennas;
Guard intervals in-between;
No uplink data
Writing TDD config to all 24 SDRs at the mMIMO BS

## Slide 32: mMIMO Sounder: Operation & Cleanup
mMIMO BS SDRs Power-down and Cleanup
Saving HDF5 logs
4 recv threads: 6 BS SDRs per thread
Client-1: Beacon detected | Send pilots
Client-2: Beacon detected | Send pilots

## Slide 33: mMIMO Sounder: Visualizations (1)
Our analysis using 1 standalone Iris client (2 Tx/Rx channels)
Log file of our current analysis (2 clients – 4 Tx/Rx channels)

## Slide 34: mMIMO Sounder: Visualizations (2)

## Slide 35: mMIMO Sounder: Visualizations (3)

## Slide 36: mMIMO Sounder: Visualizations (4)

## Slide 37: mMIMO Sounder: Visualizations (5)

## Slide 38: mMIMO Sounder: Visualizations (6)

## Slide 39: mMIMO Sounder: Visualizations (7)

## Slide 40: mMIMO Sounder with Uplink Data: Configuration
Frame schedule updated to include uplink frames from both standalone Iris clients
Modulation scheme (QAM16) for the uplink data
Other configurations remain the same

## Slide 41: mMIMO Sounder with Uplink Data: Generation (1)

## Slide 42: mMIMO Sounder with Uplink Data: Generation (2)
*Operational behavior remains the same as with the previous case (without uplink data)

## Slide 43: mMIMO Sounder with Uplink Data: Visualizations (1)
Log file for our current analysis
(48 BS antennas | 4 client antennas | With uplink data

## Slide 44: mMIMO Sounder with Uplink Data: Visualizations (2)

## Slide 45: mMIMO Sounder with Uplink Data: Visualizations (3)

## Slide 46: mMIMO Sounder with Uplink Data: Visualizations (4)

## Slide 47: mMIMO Sounder with Uplink Data: Visualizations (5)

## Slide 48: mMIMO Sounder with Uplink Data: Visualizations (6)

## Slide 49: mMIMO Sounder with Uplink Data: Visualizations (7)

## Slide 50: mMIMO Sounder with Uplink Data: Visualizations (8)

## Slide 51: Next Steps & Questions
What other experiments would we like to have done on this anechoic chamber based mMIMO testbed at POWDER?
  MATLAB toolbox based designs (see previous slide),
  Beam-Forming (Zero-Forcing/Conjugate),
  Channel Condition Number Evaluations, etc.
Are we ready to start experimenting with pi-radio: the 4x4 MIMO SDR from NYU capable of operating in the 57 – 64 GHz band?
Example paper to analyze: M. Polese, F. Restuccia, and T. Melodia, “DeepBeam: Deep Waveform Learning for Coordination-Free Beam Management in mmWave Networks,” arXiv:2012.14350, doi: 10.1145/3466772.3467035

## Slide 52: RENEW/POWDER mMIMO: MATLAB Demos

## Slide 53: MATLAB OFDM Sounder: Configuration
Number of BS Nodes = 8
Number of Clients (UEs) = 2
Tx/Rx Frequency = 3555 MHz
Tx Gain = 42 dB
Rx Gain = 20 dB
Sample Rate = 5 Msps
Number of OFDM Symbols = 44
Modulation Order = QAM16
Number of Sub-Carriers = 64
Cyclic Prefix Length = 16

## Slide 54: mMIMO MATLAB Demo: OFDM Sounder

## Slide 55: mMIMO OFDM Sounder: Tx Signal at the 2 UEs

## Slide 56: mMIMO OFDM Sounder: Rx Signal at the 8 BS nodes

## Slide 57: mMIMO OFDM Sounder: LTS Correlation at the 8 BS nodes

## Slide 58: mMIMO OFDM Sounder: Constellation Maps

## Slide 59: mMIMO OFDM Sounder: Channel Estimation

## Slide 60: mMIMO OFDM Sounder: EVM and SINR

## Slide 61
Please refer to the accompanying console logs for more details on the demodulated Rx data, beam-forming weights, SNRs (x2 UEs), and symbol/bit errors.

## Slide 62
Q & A

## Slide 63
Thank you